APPENDIX A

POTS SPLITTER SPECIFICATION

| Splitter Parameters | Value |
| --- | --- |
| Impedance | 600 Ohm+/-10%@300Ηz to 3,4khz |
| Insertion loss | -1,0dB max. @ 1.004Hz |
|  | -3,0dB @ 8,0khz |
|  | -6,0dB @ 8,5khz |
|  | -16dB @ 16khz |
|  | -100dB min. @ 22khz |
| Group delay | 200μs max. @ 0,6 to 3,2khz |
| Return loss | -20dB min @ 300Hz to 3,1khz |
| Common mode rejection ratio | -100dB min @ 0,6 to 3,2khz |
| Resistance isolation to earth | 5,0Mohms min |
| DC current carrying capability | 100mA max |
| Operating temperature | -5 to +60 degree C |
| Storage temperature | -15 to +80 degree C |
| Humidity | 10 to 90% |
| ESD discharge limits non damaging | 15KVdc |

DISTRIBUTED FILTER SPECIFICATION

| Splitter Parameters | Value |
| --- | --- |
| Matching impedance for voice terminates in accordance to G992.1 (z) | 600 Ohm resistive |
| Insertion loss. TELE port to LINE port insertion loss shall be | Less 1 dB at 1khz for Z 600 Ohm |
| Insertion loss. TELE port to LINE port insertion loss distortion term = Zcomplex(n) | 200 – 4000 Hz < + dB |
| Isolation Isolation resistance, branch-earth Isolation resistance, branch-branch DC resistance | More than 10 Μ Ohm100 V DC More than 1 Μ Ohm, 100 V DC Less than 50 Ohm |
| Signal Power Maximum peak signal power in 200-400Hz Loop current | Less than 3dBm ETS-300.001 § 4.4.2 on 600 Ohm 100mA |
| Ringing Ringing frequency Ringing AC Ringing DC (AC superimposed on DC) | 25-50 Hz Less than 100 Vrms Less than 100 V |
| Unbalance about Earth (ETS 300 001, § 4.2.1 and § 4.2.2) 15-50 Hz 50-600 Hz 600-3400 Hz | More than 40 dB terminated with 600 Ohm More than 46 dB terminated with 600 Ohm More than 52 dB terminated with 600 Ohm |
| Frequencies and levels for pulse metering (ETS 300 001 § 1.7.8) Frequency Insertion loss Maximum level | 12/16 kHz + 1% Less than 3 dB in 200 Ohm Less than 5 Vrms in 200 Ohm |

ISDN SPLITTER SPECIFICATION

| Splitter Parameters | Range | Value |
| --- | --- | --- |
| Splitter bandwidth |  | 0-94khz |
| Impedance (Z) |  | 135 Ohm |
| Modem impedance |  | 100 Ohm |
| DC voltage |  | Less than 120V |
| DC loop current |  | Less than 60mA |
| DC resistance to earth either at line or at ISDN port | 120 VDC | More than 20 M Ohm |
| Isolation resistance between A-wire end B-wire either at line or at ISDN port | 120 VDC | More than 5 M Ohm |
| Passband insertion loss requirements | 1 kHz to 40 kHz | Less than 0,8 dB |
|  | 40 kHz to 80 kHz | Less than 2 dB |
| Passband return loss requirements | 1kHz to 40 kHz | More than 16 dB |
|  | 40 kHz to 80 kHz | More than 14 dB |
| Unbalance about earth | 300 Hz to 30 kHz | More than 40 dB |
|  | 30 kHz to 1.104 MHz | More than 46 dB |
|  | 1.104 MHz to 5 MHz | More than 40 dB |
| Delay distortion | 100 Hz to 80 kHz | Less than 20 μsec |
| Isolation requirements | 150 kHz to 1.104 MHz | More than 65 dB |
| ADSL insertion loss | 120 kHz to 170 kHz | Less than 3 dB |
|  | 170 kHz to 1.104 MHz | Less than 1 dB |